## Slide 1: FRC Java API
Who what in the where now

## Slide 2: Refresher
Objects are the basic building blocks
  They have State and Behavior
  State = variables Behavior = methods
Variables
  Can be instances of objects
  They have type  defines how the data in it is stored and how you can manipulate it

## Slide 3: The FRC Java Setup
Software
  Java SE Dev. Kit
    This guy knows what to do with the java code
  NetBeans
    The editor we type our code into
  SunSPOT Java SDK for FRC (includes WPILib)
    These are all the helper methods that are provided – free of charge

## Slide 4: Where to go for documentation
Javadoc! – verrry niiiice
  Auto generated documentation from your comments
  See the Team2168 tutorial for more info
    http://team2168.org/index.php/tutorials/89-frc-java-api-documentation?catid=54%3Aprogramming
There’s a good PDF if that’s more your style:
  “WPI Robotics Library User’s Guide”
    http://first.wpi.edu/Images/CMS/First/WPI_Robotics_Library_Users_Guide.pdf

## Slide 5: THE DEEP END
Lets get into it

## Slide 6: Default Java Programs
Starting a project – Three choices
  Simple Robot
    Code runs sequentially from start to finish
    Simple / limited
  Iterative Robot
    Methods corresponding to game mode get called repeatedly/automatically
    More complex / versatile
  Command based robot
    An extension of the iterative robot project
    Helps organize code and separate software/hardware development

## Slide 7: SimpleRobot
public class MyRobot extends SimpleRobot {
/**
* This function is called once each time the robot enters autonomous mode.
*/
public void autonomous() {
// put auto code here
}
/**
* This function is called once each time the robot enters operator control.
*/
public void operatorControl() {
//put teleop code here
}
}
Each of these methods
only gets called once
This setup is going to need a lot of loops and wait statements to get stuff done.

## Slide 8: IterativeRobot
public class MyRobot extends IterativeRobot {
/**
* This function is run when the robot is first started up and should be
* used for any initialization code.
*/
public void robotInit() {
// inintialize variable here – like begin.vi in labview
}
/**
* This function is called periodically during autonomous
*/
public void autonomousPeriodic() {
// auto code goes here
}
/**
* This function is called periodically during operator control
*/
public void teleopPeriodic() {
//teleop code goes here
}
}
Each of these methods are called w/ driver station update (~50Hz)
Contents should be quickly processed.
This setup lends itself to state machine style design

## Slide 9: Command based robot
http://firstforge.wpi.edu/sf/go/doc1297

## Slide 10: Inputs/Outputs
The cRIO has a bunch of slots for modules
The modules allow for different types of inputs and outputs to interface with the system.
Inputs tell us information about the world
  Sensors
  Commands
Outputs allow us to interact with the world
  Motors
  Relays
  Solenoids

## Slide 11: Inputs: Joystick
Joystick data read by Driver Station
Fed to robot over Eternet
Helper class: Joystick
  edu.wpi.first.wpilibj.Joystick

## Slide 12: Some details from Javadoc

## Slide 13: Inputs: Gyroscope
Measures rate of rotation relative to starting position
Measured through analog input channel
Helper class:
  edu.wpi.first.wpilibj.Gyro

## Slide 14: Some details from Javadoc

## Slide 15: Outputs (e.g. Motor)
Motors are controlled over PWM/CAN through a controller
Helper class for running the controllers: RobotDrive
  Out of the box implementations for Arcade, Tank, etc.
  edu.wpi.first.wpilibj.RobotDrive

## Slide 16: Some details from Javadoc

## Slide 17: A simple obstacle avoidance bot
Autonomous
  Use a Gyro and Ultrasonic sensor to autonomously drive around without hitting anything
  Use the following algorithm
    If you see a wall, turn 180 degrees
    otherwise drive straight
Teleoperated
  Use joystick inputs, adjusted to improve operator control